## Slide 1: Final project- Reliable multicast retransmission scheme
B06901049 林泓均
B06901096 黃昱翰

## Slide 2: Outline

## Slide 3: Contribution

## Slide 4: Contribution
Previous papers mainly focus on maximize the throughput among multicast channel.
The issue of reliability or

## Slide 5: System model
Packets Error Probability determination

## Slide 6: Parameters
Explanation | Reference Value
Transmitted power of a base station | 38 dBm(6.3W)
Maximum range a base station can transmit | 2000 m
Carrier central frequency | 3 GHz
Height of the base station | 10 m
Height of the user equipment | 1.5 m
Power spectral density of the noise | -134 dBm/Hz
Transmission gain of the transmitter and receiver | 10 dB
Rayleigh fading variance | 
Numerology (normal CP) | 2 (4 slots, 60kHz SCS)
Modulation | QPSK

## Slide 7: Error Probability determination (Assumption)
The scenario is assumed under UMi-street canyon (Urban Micro cell), NLOS.
There is only one base station(BS), and the user equipment(UE) are uniformly distributed on a circular disk.
The BS is type 1-C and an Medium Range Base Station
From TR 38.901 V16-1 Table 7.4.1-1, the pathloss model is
Using log-normal shadowing with

## Slide 8: Error Probability determination
The minimum received energy of symbol is -112dBm/Hz, defined in clause 4.4.4.2 in TS 38.521-4.
Also in TS 38.521-4, the clause 4.4.3.2 describes the noise the power spectral density as -134dBm/Hz.
The UE with SNR < 22dB will not be considered.

## Slide 9: Error Probability determination (Consider Rayleigh fading channel)
Assume the detection is coherent, and the modulation is QPSK.
The bit error rate should be

## Slide 10: Error Probability determination (Consider Channel Coding)

## Slide 11: System model
Retransmission scheme

## Slide 12: Parameters

## Slide 13: Intro to retransmission
Despite of the channel coding, the transmission may fail if we only transmitted once.
To maintain the reliability, retransmission is essential.
Three typical retransmission scheme
  Blind retransmission
  Nack-based retransmission
  HARQ retransmission
In multicast scenario, we usually consider to use blind retransmission and nack-based retransmission

## Slide 14: Blind Retransmission
BS will transmit all needed packets without feedback.
Assume there are no round trip time (RTT) in blind retransmission.
Bad at resource utilization, but merely having latency.
Already used in lots of low latency requirement application, such as V2X.
To reach the constraint of reliability, the transmission packets number for a single packet can be determined by selecting the minimum which satisfy the following inequality

## Slide 15: Blind Retransmission

## Slide 16: Mathematical derivation
The UE doesn’t need more same packets after successfully decoding the packet
  The r.v. of needed packets for a UE to successfully decode is , and the PMF is
The r.v. for number of duplicated packet needed to be transmitted in multicast is
The probability of successfully transmitting a packet with x transmission is
To satisfy the constraint of reliability for all packets, we have
Find the minimum by testing the above inequality iteratively, and that is the desired .

## Slide 17: Nack-based Retransmission

## Slide 18: Nack-based Retransmission

## Slide 19: Nack-based retransmission with XOR coding
To improve our efficiency, the network coding can be applied.
Assume two packets, p1 and p2, are transmitted in one time slot. If we XOR the both packets, we can get a new packet, called as p3.
If p1, p2 and p3 are transmitted, although a UE failed to decode the p1, it still can get the information of p1 by XORing p2 and p3 (p1 XOR p2), if p2 and p3 are successfully decoded.
  This is due to the fact that
Transmitting p3 is similar with transmitting p1 and p2, while it only costs one resource block.

## Slide 20: Nack-based retransmission with XOR coding

## Slide 21
Assume for the BS, the following information are known and determined
  Latency Constraint
  Reliability Constraint
  Packet error rate for each UE
The things that BS should decide
  Which scheme to use? (blind retransmission or nack-based retransmission)
  How many packets

## Slide 22: Result

## Slide 23: Total

## Slide 24: Conclusion

## Slide 25
For the fixed amount of packets, N,

## Slide 26: Future Work
Consider different modulation and coding scheme (MCS)
  Isolate the bottleneck UE to improve the total latency.
  For the UE with better channel quality, higher MCS can be applied.
  The total resource usage will increase.
Fountain code
  Here we only consider the XOR of the packets.
  In the multicast scenario, some network coding schemes, such as Raptor code, are used.
  For total n packets, a UE can decode the data after receiving arbitrary k packets (n>=k).
Combine with the dual connectivity.
  Assume the UE can receive the signal from two base station.
  What may be the best receiving scheme for the UE ?

## Slide 27: Reference
J. Du, W. Zhu, J. Xu, Z. Li and H. Wang, ”A Compressed HARQ Feed-back for Device-to-Device Multicast Communications,” 2012 IEEE Vehicular Technology Conference
F. Takahashi and K. Higuchi, ”HARQ for Predetermined-Rate Multicast Channel,” 2010 IEEE 71st Vehicular Technology Conference
J. Kim, H. Jin, D. K. Sung and R. Schober, ”Optimization of Wireless Multicast Systems Employing Hybrid-ARQ with Chase Combining,” in IEEE Transactions on Vehicular Technology